## Slide 1: UVM Sans UVM An approach to automating UVM testbench writing
Rich Edelman, Mentor
Shashi Bhutada, Mentor

## Slide 2: Goal: Better Verification  Use UVM
More stimulus with less effort
  Constraints
  Seeds
Functional coverage
  Some
  Better
Simpler abstraction for thinking about tests
Simpler adoption of SystemVerilog
Management thinks UVM is a “good idea”
Resume update
DUT
ABC
Agent
XYZ
Agent

## Slide 3: UVM Vocabulary
OOP
Configuration database
Resource database
Factory
Phases
Components
Objects
Macros!
Transactions
Sequences
Sequencers
Sequence Items
Randomization and Constraints
Agents
Environments
Tests
Virtual Interfaces
uvm_info & VERBOSITY

## Slide 4: Learning the UVM is like Learning to Drive
Perilous
Rules  DMV / CHP
Can be Tedious
  Classroom class
  Behind the wheel class
  60 hours practice
Try it out
  Sunday morning
  Safe work parking lot and business park
Get more brave
  Country road/Straight line driving…
  Long drive to Yosemite
  Glacier Point Road!
Maps!! Guides
  Reference material

## Slide 5: Learning to Drive Learning the UVM
Pushback
  Kids these days…. They don’t want to drive…
    “Dad, You’ll just make me run errands”
  Will the UVM improve my verification?
    What’s the Return on Investment?
Driving and the UVM
  Independence
  Responsibility
  Productivity
  Flexibility
  Exploring new spaces
Driving Results – 10 months later
Really good driver
Really big smiles
UVM Results – 3-8 hours later
Random traffic
Simple functional coverage

## Slide 6: Better Verification with UVM
Training
Learning curve
Practice
Becoming an expert
Google Street View – Glacier Point

## Slide 7: What to do next?

## Slide 8: Automation
What if we had a template and a generator?
What if we had a framework?
What if we had a way to come up running a UVM testbench in a day? (or less)

## Slide 9: Who might use a generator + template?
Block tester
Non-UVM user
New-UVM user
UVM user tired of typing all the boilerplate
There are
  Many successful templates
  Many successful generators
  Google
    “Easy UVM”, “UVM Framework”, “UVM Template”

## Slide 10: Still need a little bit of UVM
An agent manages an interface
An environment is a simple container for agents
A test constructs an environment, configures it and starts sequences running on the agents
A sequence is a program which creates transactions and sends them to the driver
A driver takes a transaction and causes pin wiggles.
A monitor watches pin wiggles and creates transactions.

## Slide 11: A UVM Agent
DUT
ABC
Agent
XYZ
Agent
TEST_TOP
ENV
XYZ Agent
Driver
Monitor
Sequencer
Coverage
Sequence
ABC Agent
Driver
Monitor
Sequencer
Coverage
Sequence
BFM
SB
TOP
DUT
BFM

## Slide 12: What’s really going on?
BFM
& Interface
Sequence
transaction
Driver
Sequencer
creates
orders
executes
start_item(t)
finish_item(t)
get_next_item(t))
item_done()
Monitor
Coverage
transaction
recognizes & creates
sampled
ap.write(t)
sample(t)
Notes: A Sequence creates a Transaction and sends it to the Sequencer, which forwards it to the Driver.
The Driver calls the BFM to wiggle the pins according to the Transaction it received.

## Slide 13: A UVM Testbench Generator
The generator is not the goal.
  Keep it simple
  Copy the AGENT, changing names
  Copy the env, test, top, etc.
#!/bin/csh -f
mkdir -p GENERATED
foreach agent ( ABC XYZ )
tar cf - -C uvm-templates \
--transform=s/MY_AGENT_/${agent}_/g \
agents/MY_AGENT_agent \
| tar xvf - -C GENERATED
pushd GENERATED/agents/${agent}_agent
foreach file ( `find . -type f ` )
sed -e s/MY_AGENT_/${agent}_/g \
< $file > $file.NEW
mv $file.NEW $file
end
popd
end
tar cf - \
-C uvm-templates \
env/env.svh \
env/test_0.svh \
env/test_pkg.sv \
tb/dut_wrapper.sv \
tb/test_top.sv \
tb/top.sv \
sim/makefile \
| tar xvf - \
-C GENERATED
Generator Eye Test
ABC
XYZ
tb
MY_
tb
ABC
XYZ
tb
Hand Edit
tar and sed
Templates
Generated Code
My New Testbench

## Slide 14: A UVM Testbench Template
The template is Runnable!
uvm-templates/
├── env
│ ├── env.svh
│ ├── test_0.svh
│ └── test_pkg.sv
├── rtl
├── sim
│ └── makefile
└── tb
├── dut_wrapper.sv
├── test_top.sv
└── top.sv
uvm-templates/
├── agents
│ └── MY_AGENT_agent
│ ├── MY_AGENT_agent.svh
│ ├── MY_AGENT_agent_pkg.sv
│ ├── MY_AGENT_config.svh
│ ├── MY_AGENT_coverage.svh
│ ├── MY_AGENT_driver.svh
│ ├── MY_AGENT_if.svh
│ ├── MY_AGENT_monitor.svh
│ ├── MY_AGENT_seq.svh
│ ├── MY_AGENT_seq_item.svh
│ └── MY_AGENT_sequencer.svh
18 files, 544 lines of code

## Slide 15: A UVM Testbench Generated
Name changes… MY_AGENT  ABC_ / XYZ_
testbench/
+-- agents
¦ +-- ABC_agent
¦ ¦ +-- ABC_agent.svh
¦ ¦ +-- ABC_agent_pkg.sv
¦ ¦ +-- ABC_config.svh
¦ ¦ +-- ABC_coverage.svh
¦ ¦ +-- ABC_driver.svh
¦ ¦ +-- ABC_if.svh
¦ ¦ +-- ABC_monitor.svh
¦ ¦ +-- ABC_seq.svh
¦ ¦ +-- ABC_seq_item.svh
¦ ¦ +-- ABC_sequencer.svh
testbench/
+-- agents
¦ +-- XYZ_agent
¦ +-- XYZ_agent.svh
¦ +-- XYZ_agent_pkg.sv
¦ +-- XYZ_config.svh
¦ +-- XYZ_coverage.svh
¦ +-- XYZ_driver.svh
¦ +-- XYZ_if.svh
¦ +-- XYZ_monitor.svh
¦ +-- XYZ_seq.svh
¦ +-- XYZ_seq_item.svh
¦ +-- XYZ_sequencer.svh
testbench/
├── env
│ ├── env.svh
│ ├── test_0.svh
│ └── test_pkg.sv
├── sim
│ └── makefile
└── tb
├── dut_wrapper.sv
├── test_top.sv
└── top.sv
28 files, 1400 lines of code

## Slide 16: Your bus Write an interface
Your bus, Your pins. Collected together in a bundle
interface ABC_if ( input CLK );
logic RST;
logic VALID; // Goes high when the addr/data is valid.
logic READY; // Goes high when the DUT is ready.
logic RW; // READ = 1, WRITE = 0
logic BURST; // High when a burst begins, low when it ends.
logic [31:0] ADDR;
logic [31:0] DATAI;
wire [31:0] DATAO;
endinterface
TEST_TOP
ENV
XYZ Agent
Driver
Monitor
Sequencer
Coverage
Sequence
ABC Agent
Driver
Monitor
Sequencer
Coverage
Sequence
BFM
SB
TOP
DUT
BFM
Your Bus

## Slide 17: Write a BFM interface
BFM “helper” routines
interface ABC_bfm ( ABC_if bus );
task reset();
task read( bit[31:0] addr, output bit[31:0] data);
task write(bit[31:0] addr, input bit[31:0] data);
task burst_read( bit[31:0] addr, output bit[31:0] data[4]);
task burst_write(bit[31:0] addr, bit[31:0] data[4]);
task monitor(output bit transaction_ok,
bit rw, bit [31:0] addr, bit [31:0] data[4], bit burst);
endinterface: ABC_bfm
TEST_TOP
ENV
XYZ Agent
Driver
Monitor
Sequencer
Coverage
Sequence
ABC Agent
Driver
Monitor
Sequencer
Coverage
Sequence
BFM
SB
TOP
DUT
BFM
Your BFM

## Slide 18: Write a BFM write()
write(addr, data)
task write(bit[31:0] addr, input bit[31:0] data);
bus.RW <= 0;
bus.BURST <= 0;
bus.ADDR <= addr;
bus.DATAI <= data;
bus.VALID <= 1;
@(posedge bus.CLK);
while (!bus.READY)
@(posedge bus.CLK);
bus.VALID <= 0;
endtask
TEST_TOP
ENV
XYZ Agent
Driver
Monitor
Sequencer
Coverage
Sequence
ABC Agent
Driver
Monitor
Sequencer
Coverage
Sequence
BFM
SB
TOP
DUT
BFM
Call write() to cause
a write transaction

## Slide 19: Write a BFM monitor()
task monitor(output bit transaction_ok,
bit rw, bit [31:0] addr, bit [31:0] data[4], bit burst);
@(negedge bus.CLK);
if ((bus.READY == '1) && (bus.VALID == '1) &&
(bus.BURST == '0)) begin
burst = 0;
rw = bus.RW;
addr = bus.ADDR;
@(posedge bus.CLK);
if (rw == 1) // READ
data[0] = bus.DATAO;
else // WRITE
data[0] = bus.DATAI;
transaction_ok = 1;
end
endtask
TEST_TOP
ENV
XYZ Agent
Driver
Monitor
Sequencer
Coverage
Sequence
ABC Agent
Driver
Monitor
Sequencer
Coverage
Sequence
BFM
SB
TOP
DUT
BFM

## Slide 20: Write a transaction
What is your test abstraction?
  READ/WRITE
  READ/WRITE Registers
  “Direct Map”
    signals == transaction
What constraints are needed?
class ABC_seq_item extends uvm_sequence_item;
rand bit burst;
rand bit rw;
rand bit[31:0] addr;
rand bit[31:0] data[4];
constraint val_addr { addr >= 0; addr <= 136; }
endclass
interface ABC_if (...);
logic RST;
logic VALID;
logic READY;
logic RW;
logic BURST;
logic [31:0] ADDR;
logic [31:0] DATAI;
wire [31:0] DATAO;
endinterface
TEST_TOP
ENV
XYZ Agent
Driver
Monitor
Sequencer
Coverage
Sequence
ABC Agent
Driver
Monitor
Sequencer
Coverage
Sequence
BFM
SB
TOP
DUT
BFM
Your
Bus

## Slide 21: Some coverage
class ABC_coverage extends
uvm_subscriber #(ABC_seq_item);
ABC_seq_item t;
covergroup cg;
burst_cp: coverpoint t.burst;
rw_cp: coverpoint t.rw;
...
endgroup
virtual function void sample(ABC_seq_item t);
this.t = t;
cg.sample();
endfunction
function void write(ABC_seq_item t);
sample(t);
`uvm_info("COVERAGE", $sformatf("Coverage=%0d%% (t=%s)",
cg.get_inst_coverage(), t.convert2string()), UVM_MEDIUM)
endfunction
endclass
class ABC_seq_item ...
rand bit burst;
rand bit rw;
rand bit[31:0] addr;
rand bit[31:0] data[4];
endclass
TEST_TOP
ENV
XYZ Agent
Driver
Monitor
Sequencer
Coverage
Sequence
ABC Agent
Driver
Monitor
Sequencer
Coverage
Sequence
BFM
SB
TOP
DUT
BFM
Your
Transaction

## Slide 22: Write a driver
class ABC_driver extends uvm_driver#(ABC_seq_item);
virtual ABC_bfm bfm;
task run_phase(uvm_phase phase);
ABC_seq_item item;
forever begin
seq_item_port.get_next_item(item);
`uvm_info("DRIVER",
$sformatf("item=%s", item.convert2string()),
UVM_MEDIUM)
if (item.rw == 1)
bfm.read(item.addr, item.data[0]);
else
bfm.write(item.addr, item.data[0]);
seq_item_port.item_done();
end
endtask
endclass: ABC_driver
TEST_TOP
ENV
XYZ Agent
Driver
Monitor
Sequencer
Coverage
Sequence
ABC Agent
Driver
Monitor
Sequencer
Coverage
Sequence
BFM
SB
TOP
DUT
BFM
Convert a transaction
into a BFM call
Notes: Get a transaction
Apply the transaction to the pins/bus/interface

## Slide 23: Write a monitor
class ABC_monitor extends uvm_monitor;
virtual ABC_bfm bfm;
uvm_analysis_port #(ABC_seq_item) ap;
function void build_phase(uvm_phase phase);
ap = new("ap", this);
endfunction
task run_phase(uvm_phase phase);
ABC_seq_item t;
forever begin
t = ABC_seq_item::type_id::create("t");
bfm.monitor(t.rw, t.addr, t.data, t.burst);
ap.write(t);
end
endtask
endclass: ABC_monitor
TEST_TOP
ENV
XYZ Agent
Driver
Monitor
Sequencer
Coverage
Sequence
ABC Agent
Driver
Monitor
Sequencer
Coverage
Sequence
BFM
SB
TOP
DUT
BFM
Monitoring the bus
with the BFM Monitor
Notes: Recognize a transaction
Build a “class”, publish it out an analysis port

## Slide 24: Write a sequence
class ABC_seq extends uvm_sequence #(ABC_seq_item);
int number_of_items = 100;
rand bit[31:0] addr, addr_low, addr_high;
constraint rand_range {addr_low>='h00; addr_high<='h82;
addr_low<addr_high;}
task body();
ABC_seq_item item;
for(int i = 0; i < number_of_items; i++) begin
item = ABC_seq_item::type_id::create("item");
start_item(item);
item.randomize() with {addr>=local::addr_low;
addr<=local::addr_high;};
finish_item(item);
end
endtask
endclass: ABC_seq
TEST_TOP
ENV
XYZ Agent
Driver
Monitor
Sequencer
Coverage
Sequence
ABC Agent
Driver
Monitor
Sequencer
Coverage
Sequence
BFM
SB
TOP
DUT
BFM
Generating “N” transactions
Spend time here

## Slide 25: Env – good template
class env extends uvm_env;
ABC_agent ABC_1_agent_h;
ABC_config ABC_1_config_h;
XYZ_agent XYZ_2_agent_h;
XYZ_config XYZ_2_config_h;
function void build_phase(uvm_phase phase);
ABC_1_agent_h = ABC_agent::type_id::create( "ABC_1_agent_h", this);
ABC_1_config_h = ABC_config::type_id::create( "ABC_1_config_h", this);
uvm_config_db #(virtual ABC_bfm)::get(null,"","ABC_1_bfm", ABC_1_config_h.bfm);
ABC_1_agent_h.config_h = ABC_1_config_h;
... XYZ
endfunction: build_phase
endclass: env
TEST_TOP
ENV
XYZ Agent
Driver
Monitor
Sequencer
Coverage
Sequence
ABC Agent
Driver
Monitor
Sequencer
Coverage
Sequence
BFM
SB
TOP
DUT
BFM
The “environment” – 2 connections

## Slide 26: DUT Wrapper
Connect pins to interface
module dut_wrapper(
ABC_if ABC_1_if,
XYZ_if XYZ_2_if
);
dut_mem u_dut(
.CLK1 (ABC_1_if.CLK),
.RST1 (ABC_1_if.RST),
.RW1 (ABC_1_if.RW),
.READY1(ABC_1_if.READY),
.VALID1(ABC_1_if.VALID),
.ADDR1 (ABC_1_if.ADDR),
.DATAI1(ABC_1_if.DATAI),
.DATAO1(ABC_1_if.DATAO),
.CLK2 (XYZ_2_if.CLK),
.RST2 (XYZ_2_if.RST),
.RW2 (XYZ_2_if.RW),
.READY2(XYZ_2_if.READY),
.VALID2(XYZ_2_if.VALID),
.ADDR2 (XYZ_2_if.ADDR),
.DATAI2(XYZ_2_if.DATAI),
.DATAO2(XYZ_2_if.DATAO)
);
endmodule: dut_wrapper
TEST_TOP
ENV
XYZ Agent
Driver
Monitor
Sequencer
Coverage
Sequence
ABC Agent
Driver
Monitor
Sequencer
Coverage
Sequence
BFM
SB
TOP
DUT
BFM
Connectivity

## Slide 27: Top
module top;
ABC_if ABC_1_if (.CLK(clock));
XYZ_if XYZ_2_if (.CLK(clock));
dut_wrapper dut1 (
.ABC_1_if(ABC_1_if),
.XYZ_2_if(XYZ_2_if)
);
endmodule: top
TEST_TOP
ENV
XYZ Agent
Driver
Monitor
Sequencer
Coverage
Sequence
ABC Agent
Driver
Monitor
Sequencer
Coverage
Sequence
BFM
SB
TOP
DUT
BFM
Instantiate your RTL
and your interfaces

## Slide 28: Test Top
module test_top;
import uvm_pkg::*;
import test_pkg::*;
ABC_bfm ABC_1_bfm (top.ABC_1_if);
XYZ_bfm XYZ_2_bfm (top.XYZ_2_if);
initial begin
uvm_config_db#(virtual ABC_bfm)::set(null, "", "ABC_1_bfm", ABC_1_bfm);
uvm_config_db#(virtual XYZ_bfm)::set(null, "", "XYZ_2_bfm", XYZ_2_bfm);
run_test();
end
endmodule: test_top
TEST_TOP
ENV
XYZ Agent
Driver
Monitor
Sequencer
Coverage
Sequence
ABC Agent
Driver
Monitor
Sequencer
Coverage
Sequence
BFM
SB
TOP
DUT
BFM
Details connecting RTL to class

## Slide 29: Summary
Use automation  a generator, framework, template
Build (hand edit) your
  Bus(interface), Transaction, Driver and Monitor
  Constraints
  Functional coverage
Enjoy your new High Performance Testbench
Questions?
Contact rich_edelman@mentor.com
And Drive Safely!
Notes: Whether learning to drive or learning to build UVM testbenches, stay safe, and you’ll be happy….